## Slide 1: Securing and Scaling the Network Infrastructure for MLK
Network Design and Implementation for multi branch Campus

## Slide 2: Introduction
Overview of ITC University
  Operates across two campuses.
  Serves approximately 25,000 users.
Growth Projections
  Anticipated doubling of users by 2030.
Project Goal
  Design and implement a scalable, secure, and reliable network infrastructure.

## Slide 3: Project Objectives
Network Scalability
  Design a network capable of accommodating a growing user base.
Security
  Implement robust security measures to protect data.
Redundancy
  Ensure high availability and minimize downtime.
Seamless Connectivity
  Facilitate secure communication between campuses.
Robust Management
  Manage the network with VLANs, firewalls, and access controls.

## Slide 4: Network Design Overview
Hierarchical Design Model
  Enhances scalability, redundancy, and ease of management.
Three Layers of the Design
  Core Layer: Centralized management using multilayer switches (Catalyst 3650).
  Distribution Layer: Interconnects various VLANs and enables inter-VLAN routing.
  Access Layer: Connects individual faculties and departments using Catalyst 2960 switches.

## Slide 5: Key Protocols and Technologies
Routing and Switching Protocols
  OSPF for dynamic routing.
  LACP EtherChannel for increased bandwidth.
  HSRP for redundancy and high availability.
Traffic Management and Security
  STP PortFast and BPDUguard to prevent loops.
  ACLs for traffic management.
Network Addressing
  NAT for IP management.

## Slide 6: VLAN Segmentation
Purpose of VLANs
  Increase security and improve network performance.
VLAN Assignments
  VLAN 10: Management (192.168.10.0/24)
  VLAN 20 & 60: LAN (172.16.0.0/16, 172.17.0.0/16)
  VLAN 50 & 90: WLAN (10.10.0.0/16, 10.11.0.0/16)
  VLAN 199: Blackhole VLAN for unused ports.
Inter-VLAN Routing
  Achieved via core multilayer switches.

## Slide 7: Implementation Phases Overview
Phases of Implementation
  A systematic approach to project execution.
Key Goals of Each Phase
  Planning, design, configuration, and security enhancements.

## Slide 8: Phase 1 - Planning and Requirements Gathering
Goals
  Identify current and future network requirements.
Key Actions
  Meetings with university IT staff to assess operational needs.
  Evaluation of the current infrastructure for scalability.

## Slide 9: Phase 2 - Network Design and Scalability Considerations
Design Highlights
  Implemented EtherChannel (LACP) for link aggregation.
  Enabled STP PortFast and BPDUguard for network protection.
Future Growth
  Designed to support up to 50,000 users by 2030.

## Slide 10: Phase 3 - Hardware and Software Configuration
Hardware Setup
  Cisco ASA 5506-X firewalls.
  Catalyst 3650 and 2960 switches.
  Wireless LAN Controllers (WLC) for managing access points.
Software Setup
  Configured OSPF routing protocol for dynamic routing.
  Established basic security settings (hostnames, passwords, SSH).

## Slide 11: Phase 4 - Security Enhancements
Goals
  Ensure secure communication across the network.
Key Actions
  Configuration of Cisco ASA Firewalls for security zones.
  Established ACLs to restrict administrative access.

## Slide 12: Key Technologies and Components
Firewalls and Security Zones
  Use of Cisco ASA 5506-X firewalls for secure segmentation.
Routing and Switching Infrastructure
  Multilayer switches for data forwarding and routing.
Wireless LAN Infrastructure
  Centrally managed wireless network with WLC.

## Slide 13: Addressing and Subnetting
Subnetting Details
  Management: 192.168.10.0/24
  WLAN: 10.10.0.0/16 (Main), 10.11.0.0/16 (Branch)
  DMZ: 10.20.20.0/27
  LAN: 172.16.0.0/16 (Main), 172.17.0.0/16 (Branch)
Public Addressing
  105.100.50.0/30 (Main), 205.200.100.0/30 (Branch)

## Slide 14: Challenges and Solutions
Challenge 1: Ensuring secure communication while maintaining performance.
  Solution: Implemented VLANs and access controls with OSPF.
Challenge 2: Providing a scalable solution for future growth.
  Solution: Designed with ample IP space and modular VLAN segmentation.

## Slide 15: Final Testing and Results
Testing Overview
  Inter-VLAN Routing: Confirmed successful communication.
  ACL and Firewall Rules: Tested security policies.
  Performance Testing: Verified speed and redundancy.

## Slide 16: Conclusion
Summary
  The network for ITC University is robust, scalable, and secure.
  Capable of handling anticipated growth and ensuring secure communication.
Future Readiness
  Prepared for future demands and technology advancements.